## Slide 1: Protein Quantitation II: Multiple Reaction Monitoring
Kelly Ruggles
kelly@fenyolab.org
New York University

## Slide 2: Traditional Affinity-based proteomics
Use antibodies to quantify proteins
  Western Blot
  RPPA
  Immunofluorescence
  Immunohistochemistry
  ELISA

## Slide 3: Mass Spectrometry based proteomic quantitation
Fractionation
Digestion
LC-MS
Lysis
MS
Shotgun proteomics
Targeted MS
1. Records M/Z
2. Selects peptides based on abundance and fragments
MS/MS
3. Protein database search for peptide identification
Data Dependent Acquisition (DDA)
Uses predefined set of peptides
1. Select precursor ion
MS
2. Precursor fragmentation
MS/MS
3. Use Precursor-Fragment pairs for identification

## Slide 4: Multiple Reaction Monitoring (MRM)
Triple Quadrupole acts as ion filters
Precursor selected in first mass analyzer (Q1)
Fragmented by collision activated dissociation (Q2)
One or several of the fragments are specifically measured in the second mass analyzer (Q3)

## Slide 5: Peptide Identification with MRM
Transition: Precursor-Fragment ion pair are used for protein identification
Select both Q1 and Q3 prior to run
  Pick Q3 fragment ions based on discovery experiments, spectral libraries
  Q1 doubly or triply charged peptides
Use the 3 most intense transitions for quantitation
Q1
Q2
Q3
Mass Select
Precursor
Fragment
Mass Select
Fragment Ion
Transition

## Slide 6: Label-free quantification
Usually use 3 or more precursor-product ion pairs (transitions) for quantitation
Relies on direct evaluation of MS signal intensities of naturally occurring peptides in a sample.
Simple and straightforward
Low precision
Several peptides for each protein should be quantified to avoid false quantification

## Slide 7: Stable Isotope Dilution (SID)
Use isotopically labeled reference protein
13C and/or 15N labeled peptide analogs
Chemically identical to the target peptide but with mass difference
Add known quantity of heavy standard
Compare signals for the light to the heavy reference to determine for precise quantification
H
L
Fractionation
Digestion
LC-MS
Light
Lysis
Synthetic
Peptides
(Heavy)
MS

## Slide 8: Fragment Ion Detection and Protein Quantitation
Meng Z and Veenstra TD, 2011
Heavy
Light
Q1
Q3

## Slide 9: Quantification Details
PAR = Light (Analyte) Peak Area
Heavy (SIS) Peak Area
H
L
MS
Analyte
SIS
SIS: Stable Isotope Standard
PAR: Peak Area Ratio
-Use at least 3 transitions
-Have to make sure these transitions do not have interferences
Analyte concentration= PAR*SIS peptide concentration

## Slide 10: Strengths of MRM
Can detect multiple transitions on the order of 10msec per transition
Can analyze many peptides (100s) per assay and the monitoring of many transitions per peptide
High sensitivity
High reproducibility
Detects low level analytes even in complex matrix
Golden standard for quantitation!

## Slide 11: Weaknesses of MRM
Focuses on defined set of peptide candidates
  Need to know charge state, retention time and relative product ion intensities before experimentation
Physical limit to the number of transitions that can be measured at once
  Can get around this by using time-scheduled MRM, monitor transitions for a peptide in small window near retention time

## Slide 12: Parallel Reaction Monitoring (PRM)
Q3 is substituted with a high resolution mass analyzer to detect all target product ions
Generates high resolution, full scan MS/MS data
All transitions can be used to confirm peptide ID
Don’t have to choose ions beforehand
Peterson et al., 2012

## Slide 13: SWATH-MS: Data Collection
32 discrete precursor isolation windows of
25–Da width across the 400-1200 m/z range
Gillet et al., 2012
Data acquired on quadrupole-quadrupole TOF high resolution instrument cycling through 32-consecutive 25-Da precursor isolation windows (swaths).
Generates fragment ion spectra for all precursor ions within a user defined precursor retention time and m/z
Records the fragment ion spectra as complex fragment ion maps

## Slide 14: Applications of MRM
Protein complex
subunit stoichiometry
Metabolic pathway analysis
Phosphorylation
Modifications within protein
Biomarkers: protein indicator correlating to a disease state

## Slide 15: MRM and Biomarker Verification
Measurable indicator that provides the status of a biological state
  Diagnosis
  Prognosis
  Treatment efficacy
Shotgun proteomics  Biomarker Discovery (<100 patients)
Targeted proteomics Biomarker Validation (~1000s patients)
  Requires higher threshold of certainty
  Remove high false positives from discovery phase
Most often plasma/serum, but can be tissue-based biomarkers
Meng Z and Veenstra TD, 2011

## Slide 16: MRM and Biomarker Verification
Originally used to analyze small molecules since the late 1970s
More recently, used for proteins and peptide quantitation in complex biological matrices
With small molecules, the matrix and analyte have different chemical natures so separation step is able to remove other components from analytes
With proteomics, both the analytes and the background matrix are made up of peptides, so this separation cannot occur. Leads to decreased sensitivity and increased interference.
Separation
MS analysis
Separation
MS analysis

## Slide 17: Enhancing MRM Sensitivity for Biomarker Discovery
Shi T., et al. 2012
Sample Enrichment
MRM3
Further fragments product ions
Reduces background
Meng Z and Veenstra TD, 2011

## Slide 18
Target Selection
Selection of peptides
Selection of transitions
Validation of transitions
Peptide Calibration Curves
MS
Target Selection
Selection of peptides
Selection of transitions
Selection/ Validation of transitions
Peptide Calibration Curves
PRM
SRM
Workflow of MRM and PRM MS/MS
Slide from Dr. Reid Townsend, Washington University in St. Louis
Notes: As Reid has discussed Parallel Reaction monitoring allows for the selection of transitions post-acquisition by collecting all transitions of each peptide and identifying “good” transitions using the data. We have developed new bioinformatics tools to aid in two steps of this analysis, the Selection of peptides and the validation of transitions post-MS acquisition.

## Slide 19
Target Selection
Selection of peptides
Selection of transitions
Validation of transitions
Peptide Calibration Curves
MS
Target Selection
Selection of peptides
Selection of transitions
Selection/ Validation of transitions
Peptide Calibration Curves
PRM
SRM
Workflow of MRM and PRM MS/MS
Define a set of proteins based on clinical/biological question

## Slide 20: Motivating Example: AKT1 and Breast Cancer
AKT
PDK
BAD
MDM2
GSK3
mTOR
RAF1

## Slide 21
Target Selection
Selection of peptides
Selection of transitions
Validation of transitions
Peptide Calibration Curves
MS
Target Selection
Selection of peptides
Selection of transitions
Selection/ Validation of transitions
Peptide Calibration Curves
PRM
SRM
Proteotypic
Consistently observed by LC-MS methods
Workflow of MRM and PRM MS/MS

## Slide 22: Selecting Peptides
A few representative peptides will be used to quantify each protein
Need to fulfill certain characteristics
  Have an unique sequence
  Consistently observed by LC-MS methods
  8-25 amino acids
  Good ionization efficiency
  m/z within the range of the instrument
  No missed cleavages
  Not too hydrophillic (poorly retained) or hydrophobic (may stick to column)

## Slide 23: Identifying Proteotypic Peptides
Set of Proteins
Peptides
Proteotypic Peptides
Step 1: Full protein sequence in FASTA format
Trypsin
Step 2: Tryptic Peptides
PTPIQLNPAPDGSAVNGTSSAETNLEALQK
LEAFLTQK
PSNIVLVNSR
LEELELDEQQR
DDDFEK…..
Step 3: Compare to human reference database
Match peptide to proteins
-Contain all peptide sequences
-Find all peptides that only map back to one gene
RefSeq
Ensembl
Uniprot
(Reference Protein DB)
Match proteins to genes
(Using protein names and genomic DB)
PTPIQLNPAPDGSAVNGTSSAETNLEALQK
LEAFLTQK
PSNIVLVNSR
LEELELDEQQR
DDDFEK…..

## Slide 24: LC/MS Properties: GPMDB
-Compares peptides to a collection of previously observed results
-Determines how many times the peptide has been observed by others
-Most proteins show very reproducible peptide patterns

## Slide 25: LC/MS Properties: Skyline
-Compares peptides to MS/MS spectral library
-Predicts most abundant transitions

## Slide 26
Target Selection
Selection of peptides
Selection of transitions
Validation of transitions
Peptide Calibration Curves
MS
Target Selection
Selection of peptides
Selection of transitions
Selection/ Validation of transitions
Peptide Calibration Curves
PRM
SRM
Workflow of MRM and PRM MS/MS
PRM allows for selection of transitions post-data acquisition

## Slide 27: Selecting Transitions
Limitation of MRM-MS: ~1-2 m/z unit window for precursor and fragment ion occasionally let in interfering peptides with similar characteristics
If we want to use these transitions for quantitation, we need to be confident there are no interferences
Largest always largest, smallest always smallest etc.
  b-fragments of high m/z are less represented on QqQ
MRM

## Slide 28: Selecting Transitions
MRM
Peptide of interest
Interfering peptide
Limitation of MRM-MS: ~1-2 m/z unit window for precursor and fragment ion occasionally let in interfering peptides with similar characteristics
If we want to use these transitions for quantitation, we need to be confident there are no interferences
Largest always largest, smallest always smallest etc.
  b-fragments of high m/z are less represented on QqQ

## Slide 29: Selecting Transitions: SRMCollider
Input peptides of interest
Determines the m/z values for transition pair
Simulates a typical SRM experiment
Predicts fragment intensities and retention time information for input peptide
Compares the transition to all other transitions in a background proteome
Outputs the number of predicted interferences for each transition for that peptide
Input peptide sequence
Choose peptides that have at least one transition with zero interferences

## Slide 30
Can use to find best transitions to pick
  Intensity (rank)
  Dot product (similarity to reference spectra)
Want high rank and dotp close to 1
Selecting Transitions: Skyline

## Slide 31
Target Selection
Selection of peptides
Selection of transitions
Validation of transitions
Peptide Calibration Curves
MS
Target Selection
Selection of peptides
Selection of transitions
Selection/ Validation of transitions
Peptide Calibration Curves
PRM
SRM
Workflow of MRM and PRM MS/MS

## Slide 32: Validating Transitions: Contrast Angle
Spectral Contrast Angle: each spectrum represented as a vector in N-dimensional space
Spectra that resemble each other have vectors pointing in the same direction (θ ~ 0°)
Analyte
SIS
b1
a1
b2
a2
ra
rb

## Slide 33: Validating Transitions: “Branching ratio”
Branching Ratio (BR): ratio of the peak intensities
IAx, IBx : Peak areas of Analyte
IAxS, IBxS : Peak areas of SIS
n=number of SIS transitions
Light (Analyte)
Heavy(SIS)
I1
I2
I1
I2
I3
I3
Kushnir, 2005

## Slide 34
AuDIT: Automated Detection of Inaccurate and imprecise Transitions
Uses “branching ratio”
1. Calculate relative ratios of each transition from the same precursor
2. Apply t-test to determine if relative ratios of analyte are different from relative ratios of SIS
http://www.broadinstitute.org/cancer/software/genepattern/modules/AuDIT.html.
Validating Transitions in MRM: AuDIT

## Slide 35: Validating Transitions in MRM: AuDIT
Abbatiello, 2009
Relative product ions should have a constant relationship
Blue: Light
Red: Heavy

## Slide 36: Validating Transitions in PRM: CRAFTS
PRM and MRM are most useful when quantifying protein in a complex matrix
  Tumor lysate
  Plasma
Simple Matrix (buffer) should have no interferences
Compare the transitions in complex to those in simple
Ratio close to 1 indicates low interference

## Slide 37
Light
Simple
Complex
Heavy
MATRIX
PEPTIDE
Simple matrix: peptide carrier solution
Complex matrix: unfractionated tumor digest
Simple matrix should have minimal interference- use this as reference
Transitions in complex buffer should have the same relative intensities of transitions within the spectra
Transitions in complex with relative intensities different from simple  interference
Validating Transitions in PRM: CRAFTS

## Slide 38: Validating Transitions in PRM: CRAFTS
Light
Simple
Complex
100
150
40
220
60
90
Transition | Simple | Complex
y2 | 100 | 150
y5 | 40 | 220
y10 | 60 | 90
 | y2 | y5 | y10
y2 | 1 | 1.47 | 0.6
y5 | 0.68 | 1 | 0.41
y10 | 1.67 | 2.44 | 1
 | y2 | y5 | y10
y2 | 1 | 0.4 | 0.6
y5 | 2.5 | 1 | 1.5
y10 | 1.67 | 0.67 | 1
 | y2 | y5 | y10
y2 | 1 | y5/y2 | y10/y2
y5 | y2/y5 | 1 | y10/y5
y10 | y2/y10 | y5/y10 | 1
Ratio of Transitions
Simple
Matrix
Complex
Matrix

## Slide 39
 | y2 | y5 | y10
y2 | 1 | y5/y2 | y10/y2
y5 | y2/y5 | 1 | y10/y5
y10 | y2/y10 | y5/y10 | 1
Ratio of Transitions
Simple
Matrix
Complex
Matrix
 | y2 | y5 | y10
y2 | 1 | 1.47 | 0.6
y5 | 0.68 | 1 | 0.41
y10 | 1.67 | 2.44 | 1
 | y2 | y5 | y10
y2 | 1 | 0.4 | 0.6
y5 | 2.5 | 1 | 1.5
y10 | 1.67 | 0.67 | 1
Complex/Simple
 | y2 | y5 | y10
y2 | 1 | 3.675 | 1
y5 | 0.272 | 1 | 0.273
y10 | 1 | 3.641 | 1
Validating Transitions in PRM: CRAFTS

## Slide 40: Validating Transitions in PRM: CRAFTS
Simple
Heavy
Complex
Complex/Simple
(Combinatorial Ratio)
Light
Simple
Complex
Ratio of transitions (Branching Ratio)
Visualize Complex/Simple
Choose “good” transitions
Minimal Interference: y3, y4, b3, y5, y6, y7, b6, b7, y8
Minimal Interference: y3, y4, b3, y5, y6, y7, y10, y11
<= Threshold
> Threshold

## Slide 41: Validating Transitions in PRM: CRAFTS
Light
Heavy
Minimal Interference: y3, y4, b3, y5, y6, y7, b6, b7, y8
With Interference: y9, y11
Minimal Interference: y3, y4, b3, y5, y6, y7, y10, y11
With Interference: y8, y9
Use highlighted values to get mean ratio

## Slide 42: CRAFTS: Ranking Transitions by Mean Combinatorial Ratio

## Slide 44: Open Source MRM analysis tools

## Slide 45: SKYLINE for creating targeted MS/MS methods
Skyline digests proteins and fragments peptides and uses spectral library to find transition intensity

## Slide 46: Skyline for MRM: Method Building
Input all peptides of interest
Shows graphs of MS/MS spectra from spectral library

## Slide 47: Skyline for MRM: Method Building
Helps generate protetypic peptide lists using MS/MS spectral libraries
Find which peptides can be measured in specific matrix
Find best transitions to measure for a peptide
Creates transition lists and vendor-specific instrument methods for MRM experiements

## Slide 48: Skyline for MRM: Quantification
Import raw files into skyline
Pick peptide of interest
Check standard peaks

## Slide 49: Skyline for MRM: Quantification
Use the heavy standard PAR to make calibration curve
Determine sample quantity based on curve

## Slide 50: Questions?

## Slide 51: MRM Instrumentation
Quadrupole Time-of-Flight (Qqtof)
Triple Quadrupole